## Slide 1
PACKET ROUTING SYSTEM
4-Port Router with Round-Robin Arbitration
Course: Digital IC Design Using FPGA
Youssef Hossam Eldeen · Mohamed Elzainy · Fares Nagah Ibrahim · Yehia Omar

## Slide 2
Packet Routing System · Digital IC Design Using FPGA
2 / 8
Objective
Design and verify a 4-port packet router at the RTL level using Verilog, covering the full data path from FIFO buffering and arbitration through to packet routing and delivery.
FIFO Buffering
Four independent synchronous FIFOs (16-deep) for each input port
Round-Robin Arbiter
Fair access grant so no port is starved
Packet Routing
Destination-bit decoding steers packets to the correct output

## Slide 3
Packet Routing System · Digital IC Design Using FPGA
3 / 8
System Architecture

## Slide 4
Packet Routing System · Digital IC Design Using FPGA
3 / 8
Packet Structure

## Slide 5
Packet Routing System · Digital IC Design Using FPGA
4 / 8
Key Design Modules
Synchronous FIFO
FIFO_Memory.v · Generic WIDTH×DEPTH buffer with empty/full flags
Four FIFO Buffers
Four_FIFO_Buffers.v · Four independent 40-bit / 16-deep FIFOs
Round-Robin Arbiter
RR_Arbiter.v · State-machine grants access in rotating order
FIFO + Arbiter
FIFO_Arbiter_System.v · Integrates buffers with arbiter & mux
Packet Routing
Packet_Routing.v · Decodes destination bits, steers to output ports
Router Top
Router_TopModule.v · Top-level: Arbiter system + Packet Routing
Memory Node
ram.v · RAM slave: write / read + response packet
Network System
network.v · Router + 3 memory nodes + TB port

## Slide 6
Packet Routing System · Digital IC Design Using FPGA
5 / 8
Network System Topology

## Slide 7
Packet Routing System · Digital IC Design Using FPGA
6 / 8
RTL Schematic (Post-Synthesis)

## Slide 8
Packet Routing System · Digital IC Design Using FPGA
7 / 8
Simulation & Synthesis Results
Simulation Highlights
Write packets sent to Nodes 0, 1, 2
Read requests issued from Port 3
Responses verified on Port 3
All read-back data matched expected values
Round-robin fairness observed in waveforms
Resource Utilization
Resource | Used | Available | %
LUT | 868 | 303,600 | 0.29%
LUTRAM | 64 | 130,800 | 0.05%
FF | 1,859 | 607,200 | 0.31%
IO | 56 | 600 | 9.33%

## Slide 9
Summary
Complete 4-port packet router designed and verified in Verilog
FIFO buffering + fair round-robin arbitration + destination routing
Closed network with three memory nodes and open testbench port
Simulation confirms correct write/read transactions
Synthesized successfully with very low resource usage